OBJECTIVE : Our objective is to route a droplet from source to sink by bypassing all the obstracles in minimum Time.Here we proposed ILP fromulation for that droplet routing for Square chip electrode.

We use cross-referencing Biochip, which allows the control of an N × M grid array with only N + M control pins

ELECTRODE ACTIVATION CONSTRAINT
- EC – I : If droplet is at cell (x,y) at time t then the four diagonal a	djacent cell cannot be activated at time t+1.
- EC – II : If the droplet moves from cell (Xt ,Yt) to cell (Xt+1 ,Yt+1)	from time t to t+1 then all the 8 neighbouring cell of	(Xt+1 ,Yt+1) can’t be activated at t+1.

NOTATIONS USED IN ILP FORMULATION

1. H : Biochip height.
2. W : Biochip width.
3. T : Maximum droplet transportation time.
4. Tl : actual maximum droplet transportation time.
5. C : Set of all availabe cells.
6. D : Set of availabe diagonal cell of (x,y).
7. O : set of all obstracle cell.
8. (Sx,Sy) : Source location of the droplet .
9. (Skx,Sky) : Sink location of the droplet.
10. E5(x,y) : Set of cell (x,y) and it’s 4 adjacent cell.
11. E5(x,y) : Set of (x,y)’s 4 adjacent cell.
12. E8(x,y) : Set of cell (x,y)’s 8 adjacent cell.
13. E9(x,y) : Set of cell (x,y) and it’s 9 adjacent cell.
14. C(x,y,t) : 0/1 variable represents wheather the droplet present at cell (x,y) or not at time t.
15. LXC(t) : 0/1 variable represents column x is set to voltage low at time t.
16. HXC(t) : 0/1 variable represents column x is set to voltage high at time t.
17. Lyr(t) : 0/1 variable represents row y is set to voltage low at time t.
18. Hyr(t) : 0/1 variable represents row y is set to voltage high at time t.
19. atx,y : 0/1 variable represent cell (x,y) activated at time t.
20. b1x,y(t) : 1 means, cell (x,y) is activated and the column x is assigned to low voltage and row y is assigned to high voltage at time t.
21. b2x,y(t) : 1 means, cell (x,y) is activated and the column x is assigned to high voltage and row y is assigned to low voltage at time t.
22. dt+1x,y : 0/1 variable represent vell (x,y) is deactivated at time t.

Objective Function :
The goal is to minimize the latest time the droplet reaches to it’s sink.
minimize : Tl

Constraints of basic ILP formulation:

1. source requirement:
we assume that the droplet is present at its source location at time 0
C(Sx,Sy,0) = 1

2. Sink requirement:
The droplet must reach its sink.
sum from{t = 0} to{T} C( SK binom{}{x} ,SK binom{}{y},t) >= 1

If the droplet reach its sink it should remains there. (Let the droplet	reaches it’s sink at time t then it shoud be there at time t+1)
C(SKx,Sky,t) – C(SKx,Sky,t+1) <= 0
0<= t <T

3. Exclusivity constraint:
At each time stamp droplet can present only at one location (as we are	moving droplet from one location to oter location we don’t want to split	the droplet)
sum from{(x,y)} C( x,y,t) = 1
( x,y ) in C , 0<= t < T

4. Droplet transportation Time :
if the droplet reaches it’s sink at time t+1 , then the time when it reaches	its sink can be computed as t+1 times difference between C(x,y,t+1) and	C(x,y,t)
(t+1)((x,y,t+1) - (x,y,t) ) <= Tl	, 0<= t < T

5. static fludic constraints :
The droplet should’t present in the obstracle cell at any point of time
sum from{(x,y) in O } C( x,y,t) = 0 ,	0<= t < T

6. Dynamic fludic constraints :
when droplet moves it should’t enter into any obstracle cell. If a droplet	present in cell (x,y) at time t (Which is definately not an obstracle cell) it	should’t move to any obstracle cell at time t+1.
C(x,y,t) + sum from{(x',y') in O } C( x',y',t+1) <= 1	,0<= t < T
droplet can move any one of it’s four adjacent cell at time t+1 (droplet	can’t stall)
C(x,y,t) + sum from{(x',y') in E4(x,y) } C( x',y',t+1) <= 2 ,0<= t < T

7. Voltage assignment and cell activation:
Each row/column can be assigned one voltage (high or low) at any time.
LXC(t) + HXC(t) <= 1	0 ≤ x < W, 0 ≤ t < T
Lyr(t) + Hyr(t) <= 1	0 ≤ y < H, 0 ≤ t < T

A cell is activated if and only if it is in the intersection of a row with	high (low) voltage and a column with low (high) voltage.
(LXC(t) and Hyr(t)) or (HXC(t) and Lyr(t)) <-> atx,y	∀(x, y) ∈ C, 0 ≤ t < T

We use the following five equations and two additional variables to	linearize constraint.

LXC(t) + Hyr(t) – 2b1x,y(t) >= 0	[0+0-0 ,1+0-0,0+1-0,1+1-2]
LXC(t) + Hyr(t) – b1x,y(t) <= 1	[0+0-0 ,1+0-0,0+1-0,1+1-1]
HXC(t) + Lyr(t) – 2b2x,y(t) >= 0
HXC(t) + Lyr(t) – b2x,y(t) <= 1

cell (x,y) is activated then either b1x,y(t) = 1 or b2x,y(t) = 1 , but not both
atx,y - b1x,y(t) – b2x,y(t) = 0

b1x,y(t) = 1 means, cell (x,y) is activated and the column x is assigned to	low voltage and row y is assigned to high voltage.
b2x,y(t) = 1 means, cell (x,y) is activated and the column x is assigned to	high voltage and row y is assigned to low voltage.
Both b1x,y(t) and b2x,y(t) can’t be 1 at a time.

8. Eletrode constraint:
EC – I
C(x,y,t) + at+1x’,y’ <= 1
(x’,y’) ∈D(x,y) , 0 <= t < T
EC – II
C(x,y,t) + at+1x’,y’ <= 1	(x’,y’) ∈E8(Xt+1,Yt+1) , 0 <= t < T

(cell (x,y) is active at time t, and the droplet moves to cell (xt+1,yt+1)	at time t+1, then all the eight adjacent cell of (xt+1,yt+1) must be	deactivated at time t+1	)